## Slide 1
HOSTED BY:
SUPPORTED BY:

## Slide 2
Paper No. 183123
New Process for Complete Removal of H2S From Gas Streams and Conversion to Elemental Sulfur
Ahmed M. Shahin, Ph.D., Canada Chemical Corporation
Conrad Ayasse, PhD, FCIC, Canada Chemical Corporation
Alan Ayasse, MSc., PEng, Canada Chemical Corporation Rob Ayasse, MscEcon (IR), EMBA, Verdis Synfuels

## Slide 3
Sulfa-Niltm is an economical patented*
Dry H2S
Recovery and Conversion Process
* US 8,703,084, US 8,501,135, US 8,597,411
What is Sulfa-Niltm?

## Slide 4
Key Components of the Sulfa-niltm Process
A strong solid-state H2S absorbent
An active solid-state H2S Direct Oxidation Catalyst

## Slide 5
H2S Direct Oxidation
2 H2S + O2 → 2 S + 2 H2O
Highly exothermic reaction
Uses pure oxygen or air
Catalysts are transition metals on porous solids

## Slide 6
A packed bed
of porous solid particles
like alumina
containing a solid amine
acid gas absorbent
Sulfa-Niltm absorbent

## Slide 7
DABCO
1,4-Diazabicyclo[2.2.2]octane
Strong H2S Acid Gas Absorbent
A solid amine
Appearance | White crystalline powder
Melting point | 156 to 160 °C
Boiling point | 174 °C (345 °F; 447 K)
Solubility in water | Soluble, hygroscopic
Paper #183123 • H2S Removal & Conversion to Elemental Sulfur • Dr. Conrad Ayasse

## Slide 8
Active absorbent |  | Porous support | 
Physical state | solid | Porosity, ml/g | 1.0
Boiling point, ºC | 174 | Surface area | 270 m2/g
Chemical | Amine | Type | Alumina
Possible Sulfa-Niltm Absorbent Support

## Slide 9
H2S Stripping From Absorbent
H2S can be stripped from the absorbent at pressures higher than the raw gas temperature.
Example:
Absorb at 100 psi and strip at 400 psi.
Benefit:
Plant capital costs are reduced.
Compression costs for deep-well disposal are reduced.

## Slide 10
Feed gas
air
Gas Chromatograph
S
S
Heater
Guard
bed
D.O.
Reactor
Sulfur traps
or pits
Re-cycle
booster
MFC
MFC
Sulfa-Niltm for Low H2S Gas Streams
Solid-state H2S Absorber 1
(Saturated)
Solid-state H2S Absorber 2
(Fresh, 50 C)
Clean
gas
Red indicates the absorber stripping loop, Black the treated gas
Heater
All heat energy is provided by D.O. exotherm

## Slide 11
O2 (air)
Raw gas
Clean gas
(zero sulphur species)
Fresh re-generable H2S absorber
220+ ºC.
125 ºC
Stripped H2S (130 ºC)
Regenerating absorber
Sulfur
Direct Oxidation reactor
Steam from DO Reactor
Guard bed
50 ºC
Gas booster
Sulfa-Niltm for High H2S Gas
Decreases regeneration frequency
All heat energy is provided by D.O. exotherm

## Slide 12
  Enables low-energy dry H2S recovery from gas streams
  (Eliminates water use)
  Zero heat energy demand
  (DO reaction provides free energy)
  Operates as both a physical and a chemical H2S absorbent
  (Enables H2S stripping at elevated pressure)
  Recovers H2S at pressures above absorption pressure
  (Reduces the compression energy for deep well disposal of H2S)
  Low capital cost
  (fewer operating units
Sulfa-Niltm Process

## Slide 13
Waste Gas processing
Treats sulfur-contaminated waste gas to meet emission standards : 95+% sulfur recovery
Applications:
THAItm combustion gas
SAGD gas
Sulfa-Niltm WG

## Slide 14: Alberta Regulatory Requirements
Sulfur inlet rate (T/d) | Design Recovery Criteria (% of inlet)
1 - 5 | 70
5 - 10 | 90
10 - 50 | 96.2
50 - 2000 | 98.5 – 98.8
2000+ | 99.9
Paper #183123 • H2S Removal & Conversion to Elemental Sulfur • Dr. Conrad Ayasse

## Slide 15
Process upgrades existing Claus Tail Gas plants
Eliminates all sulfur emissions from Claus plants.
Sulfa-Niltm CTG

## Slide 16
Replaces Amine/Claus technology)
Eliminates the energy needs of Amine plants
Can operate in the presence of high CO2
Fills the sulfur removal size gap from 1-20 tonnes
Achieves sulfur-free emissions
Sulfa-Niltm C

## Slide 17
Any Questions?
To Engage With Us Further:
www.canchem.ca
www.Verdisfuels.com
Paper #183123 • H2S Removal & Conversion to Elemental Sulfur • Dr. Conrad Ayasse