## Slide 1
HOSTED BY:
SUPPORTED BY:

## Slide 2
Paper No. 183403
New Economical Process to Monetize High-CO2Natural Gas
Ahmed M. Shahin, Ph.D., Canada Chemical Corporation
Conrad Ayasse, PhD, FCIC, Canada Chemical Corporation
Alan Ayasse, MSc., PEng, Canada Chemical Corporation Rob Ayasse, MscEcon (IR), EMBA, Verdis Synfuels

## Slide 3
Target high-CO2 natural gas
Produced gas pressure is
greater than 1070 psia

## Slide 4
CO2 Removal Alternatives
Traditional amine processes-
Dilute amine solutions-high energy costs to flash a lot of water
Chemical consumption
Corrosive
Low pressure CO2: high compression costs
Cryogenic processes-
Produces liquid CO2
High energy costs for cooling and regeneration of the natural gas
Solid CO2 causes blockage of equipment
Cryogenic fluids are toxic and flammable

## Slide 5
Estimated costs of CO2 transport and storage for Natuna3, 4
(Formation at 5715 psi)
3Assessment of the capture and storage potential of CO2 co-produced with natural gas in South-East Asia, May, 2010. Asia-Pacific Economic Cooperation, APEC Energy Working Group
Gas compression capital cost is USD2.272 Billion, 38% of total capital.
Compression operating cost is USD90 Million/y,
51% of total operating cost

## Slide 6
Dry CO2 Absorption Concept
Absorbent is a packed bed
containing porous solid particles
having
absorbent polymerized inside the pores

## Slide 7
Absorbent Polymer1
An active amine adduct is formed
within the pores by reacting
a polyamine and hydrophillic polyol
crosslinked with an aldehyde
to form a thermally stable absorbent.

## Slide 8
The Reaction Of Polyethyleneimine With Polyvinylalcohol in the Presence of Acetic Acid
PEI, MW 1300 AMU
PVA, MW 85,000-124,000 AMU
Reactive secondary or tertiary amines react with CO2
Bonds to support surface
Solid polyamine
SPAA
Paper #183123 • H2S Removal & Conversion to Elemental Sulfur • Dr. Conrad Ayasse

## Slide 9
Support | Aerolyst 3038 | Aerolyst 3046
Basic compound | Aerosil 380 | Aerosil 380
Shape | Extrudates | Rings
Diameter, mm | 2.5 | OD 4.7, ID 2.0
Surface area, m2/g | 270 | 180
Pore volume, ml/g | 0.9-1.0 | 0.8-0.9
Tapped density, g/l | 400-460 | 340-400
Si content | 99.8 | 99.8
Silica Absorbent Supports

## Slide 10
CO2 Stripping at Elevated Pressure
CO2
H2S

## Slide 11
Elevated CO2 Stripping Temperature
CO2 absorbed from a gas stream at 100 psig (21 ºC.)
Is fully recovered at
300 psig (130 ºC.)

## Slide 12
Chart: Pressure, psig
| 10 | 100 | 200 | 300 | 400 | 500 | 900 | 1200
 | 0.309 | 0.965 | 1.639 | 2.316 | 2.957 | 3.562 | 6.2268 | 8.2068
CO2 Absorption Capacity
Feed gas 24.4 % CO2 in nitrogen

## Slide 13
Alternative CO2 Stripping Pressures
Desorption pressure less than Absorption pressure
Desorption pressure equal to Absorption pressure
Desorption pressure greater than Absorption pressure

## Slide 14
CO2 Phase Diagram
Critical Point:
73.77 bar (31 ºC.)
7377 kPa (1070 psia)

## Slide 15
Heating liquid CO2 and increasing its pressure converts it to a SUPERCRITICAL state: density is like a liquid and viscosity is like a gas. Cooling below the critical temperature converts it back to a liquid.
CO2 phase changes

## Slide 16
Our process exploits the ability of our absorbent to strip CO2 at pressures above 1070 psia
and
exploits phase behaviour of CO2
to
provide an economical recovery of CO2 directly as a liquid
How Does Our CO2 Recovery Plant Work?

## Slide 17
Cooler
Liquid
CO2
(<31 ºC.)
Back-
Pressure
Regulator (>1070 psia)
Absorber 1
Absorber 2
Raw Gas
Heater
Clean
Gas
Cool CO2 (<31 ºC.)
Hot CO2 (130 ºC.)
This is the starting configuration (Connections from Absorber 2 to CO2 vessels are not shown).
Absorber 1 is saturated with CO2 and Absorber 2 has begun treating Raw Gas.
Plant Starting Conditions
Pump

## Slide 18
Cooler
Liquid
CO2
(<31 ºC.)
Back-
Pressure
Regulator (>1070 psia)
Absorber 1
Absorber 2
Raw Gas
Heater
Clean
Gas
Cool CO2 (<31 ºC.)
Hot CO2 (130 ºC.)
Removing Raw Gas
Pump
Raw Gas is swept from the free space of Absorber 1 with pure cool CO2 and sent to Absorber 2 so that hydrocarbons do not contaminate the stored CO2

## Slide 19
Cooler
Liquid
CO2
(<31 ºC.)
Back-
Pressure
Regulator (>1070 psia)
Absorber 1
Absorber 2
Raw Gas
Heater
Clean
Gas
Cool CO2 (<31 ºC.)
Hot CO2 (130 ºC.)
Stripping CO2
Pump
Some stored CO2 is heated to the stripping temperature, 130 ºC, so that absorbed CO2 will be released from the bed particles and recovered . This continues until the bed is low in absorbed CO2.

## Slide 20
Cooler
Liquid
CO2
(<31 ºC.)
Back-
Pressure
Regulator (>1070 psia)
Absorber 1
Absorber 2
Raw Gas
Heater
Clean
Gas
Cool CO2 (<31 ºC.)
Hot CO2 (130 ºC.)
Flushing Hot Stripping Gas
Pump
The hot CO2 in the free space between the particles is pushed into the cooler with Raw Gas in preparation for starting the absorption cycle on Absorber 1.

## Slide 21
Cooler
Liquid
CO2
(<31 ºC.)
Back-
Pressure
Regulator (>1070 psia)
Absorber 2
Absorber 1
Raw Gas
Heater
Clean
Gas
Cool CO2 (<31 ºC.)
Hot CO2 (130 ºC.)
Switching Absorbers
Pump
The Raw Gas stream is re-directed to Absorber 1, and the CO2 stripping cycle is begun on Absorber 2.

## Slide 22
Conclusions
  Enables low-energy dry CO2 recovery
  Operates as both physical and chemical absorbent
  Recovers CO2 at pressure above absorption pressure
  Recovers CO2 from high-pressure natural gas
  as a liquid without compression

## Slide 23
Any Questions?
To Engage With Us Further:
www.canchem.ca
www.Verdisfuels.com
Paper #183403 • Monetize High CO2 Natural Gas • Dr. Conrad Ayasse